## Slide 1: Table of Contents
1 Memory Consistency
  1.1 Introduction
  1.2 Sequential Consistency
  1.3 Relaxed Consistency
2 Memory Persistency
  2.1 Terminology
  2.2 Strict Persistency
  2.3 Relaxed Persistency
References

## Slide 2: 1 内存一致性
Parallel Programming Paradigms
  Message Passing
    Distributed
    Send + onReceive
  Shared Memory
    Concurrent
    Write + Read
1.1 Introduction

## Slide 3: 1 内存一致性
A==1, C==1? | Yes, as is expected;
A==0, C==1? A==0, C==0? A==1, C==0? | Yes, for P2 may see P1’s writes in advance;
A Simple Example
  Consider the following codes:
  What are the possible outcomes?
P1
A = 0, B = 0, C = 0;
C = 1;
A = 1;
P2
while (A == 0);
B = 1;
P3
while (B == 0);
print A, C;
Initialization
Parallel
1.1 Introduction

## Slide 4: 1 内存一致性
A Simple Example
  Consider the following codes:
  What are the possible outcomes?
  Who THE HELL can tell us when values can be SEEN?
    Memory Consistency
P1
A = 0, B = 0, C = 0;
C = 1;
A = 1;
P2
while (A == 0);
B = 1;
P3
while (B == 0);
print A, C;
Initialization
Parallel
1.1 Introduction

## Slide 5: 1 内存一致性
Terminology
  Memory Consistency Model
    The policy that places an early and late bound on when a new value can be propagated to any given processor;
  Cache Coherence Protocol
    The mechanism that propagates a newly written value to the cached copies of the modified location;
Exactly the same? Nope!
1.1 Introduction

## Slide 6: 1 内存一致性
Terminology
1.1 Introduction
There DO exist architectures, though DON’T have cache, are also threatened with consistent problems.

## Slide 7: 1 内存一致性
The Definition
  [A multiprocessor system is sequentially consistent if] the result of any execution is the same as if the operations of all the processors were executed in some sequential order, and the operations of each individual processor appear in this sequence in the order specified by its program.
  Key word: program order, atomicity;
1.2 Sequential Consistency

## Slide 8: 1 内存一致性
The Definition
  [A multiprocessor system is sequentially consistent if] the result of any execution is the same as if the operations of all the processors were executed in some sequential order, and the operations of each individual processor appear in this sequence in the order specified by its program.
  Key word: program order, atomicity;
1.2 Sequential Consistency
Initially Flag1 = Flag2 = 0
P1
Flag1 = 1
if (Flag2 == 0)
critical section
P2
Flag2 = 1
if (Flag1 == 0)
critical section

## Slide 9: 1 内存一致性
The Definition
  [A multiprocessor system is sequentially consistent if] the result of any execution is the same as if the operations of all the processors were executed in some sequential order, and the operations of each individual processor appear in this sequence in the order specified by its program.
  Key word: program order, atomicity;
1.2 Sequential Consistency
Initially A = B = 0
P1
A = 1
P2
If(A == 1)
B = 1
P3
If(B == 1)
register1 = A

## Slide 10: 1 内存一致性
The Cons
  Uniprocessor compiler optimization that can result in reordering memory operations are restricted, e.g.
    Simple optimizations:
      Code motion;
      Register allocation;
      Common sub-expression elimination;
      ...
    Sophisticated optimizations:
      Loop blocking;
      Software pipelining;
      ...
  Compilers etc. : Mewww ?!
1.2 Sequential Consistency

## Slide 11: 1 内存一致性
(Ancient) Commercial System Layout
1.3 Relaxed Consistency
Simple categorization of relaxed models

## Slide 12: 1 内存一致性
TSO
  [Operations that write to memory have a total (store) order if] all processors agree on their order of execution.
    How does it relax program order:
      [√] W→R Order
      [x] W→W Order
      [x] R→RW Order
    How does it relax write atomicity:
      [x] Read Others’ Write Early
      [x] Read Own Write Early
    Safety net: RMW, membar
1.3 Relaxed Consistency
Note: →: Happened-before relation; W: Write; R: Read;

## Slide 13: 1 内存一致性
TSO
1.3 Relaxed Consistency
Note: We use M1, M2 etc. to number the instructions in the examples. Stores are written as mov [_x], val which implies that val is being stored into the memory location x. Loads are written as mov r, [_x] which implies that the contents of the memory location x are being loaded into the register r.
Processor 0 | Processor 1
mov [_x], 1 // M1 mov r1, [_y] // M2 | mov [_y], 1 // M3 mov r2, [_x] // M4
Initially x == y == 0 r1 == 0 and r2 == 0 is allowed | 
Program Order: [√] W→R Order

## Slide 14: 1 内存一致性
TSO
1.3 Relaxed Consistency
Note: We use M1, M2 etc. to number the instructions in the examples. Stores are written as mov [_x], val which implies that val is being stored into the memory location x. Loads are written as mov r, [_x] which implies that the contents of the memory location x are being loaded into the register r.
Processor 0 | Processor 1
mov [_x], 1 // M1 mov [_y], 1 // M2 | mov r1,[_y] // M3 mov r2, [_x] // M4
Initially x == y == 0 r1 == 1 and r2 == 0 is not allowed | 
Program Order: [x] W→W Order; [x] R→RW Order

## Slide 15: 1 内存一致性
TSO
1.3 Relaxed Consistency
Note: We use M1, M2 etc. to number the instructions in the examples. Stores are written as mov [_x], val which implies that val is being stored into the memory location x. Loads are written as mov r, [_x] which implies that the contents of the memory location x are being loaded into the register r.
Processor 0 | Processor 1 | Processor 2 | Processor 3
mov [_x], 1 // M1 | mov [_x], 2 // M2 | mov r1, [_x] // M3 mov r2, [_x] // M4 | mov r3, [_x] // M5 mov r4, [_x] // M6
Initially x == y == 0 r1 == 1 and r2 == 0 is not allowed |  |  | 
Atomicity: [x] Read Others’ Wirte Early

## Slide 16: 1 内存一致性
TSO
1.3 Relaxed Consistency
Note: We use M1, M2 etc. to number the instructions in the examples. Stores are written as mov [_x], val which implies that val is being stored into the memory location x. Loads are written as mov r, [_x] which implies that the contents of the memory location x are being loaded into the register r.
Processor 0 | Processor 1 | Processor 2
mov [ _x], 1 // M1 | mov r1, [ _x] // M2 mov [ _y], 1 // M3 | mov r2, [ _y] // M4 mov r3, [ _x] // M5
Initially x == y == 0 r1 == 1, r2 == 1, r3 == 0 is not allowed |  | 
Atomicity: Stores are transitively visible

## Slide 17: 1 内存一致性
TSO
1.3 Relaxed Consistency
Note: We use M1, M2 etc. to number the instructions in the examples. Stores are written as mov [_x], val which implies that val is being stored into the memory location x. Loads are written as mov r, [_x] which implies that the contents of the memory location x are being loaded into the register r.
Processor 0 | Processor 1
mov [ _x], 1 // M1 mov r1, [ _x] // M2 mov r2, [ _y] // M3 | mov [ _y], 1 // M4 mov r3, [ _y] // M5 mov r4, [ _x] // M6
Initially x == y == 0 r2 == 0 and r4 == 0 is allowed | 
Atomicity: Read Own Write Early

## Slide 18: 1 内存一致性
TSO
  Safety net: Mechanisms provided for programmers for overriding relaxations.
    [Program order appears to be maintained if] either the write or the read is already part of a read-modify-write(RMW) or is replaced by a read-modify-write.
      What is a RMW?
        ie. locked instructions in intel 64 architecture, including the implicitly locked xchg instruction and other read-modify-write instructions with a lock prefix.
1.3 Relaxed Consistency

## Slide 19: 1 内存一致性
TSO
  Safety net: Mechanisms provided for programmers for overriding relaxations.
    For TSO, program order appears to be maintained if either the write or the read is already part of a read-modify-write(RMW) or is replaced by a read-modify-write.
      What is a RMW?
      How to replace a read/write with RMW?
        Read: the write in the read-modify-write must be a “dummy” write that writes back the read value;
        Write: writing back the desired value regardless of what the read returns.
1.3 Relaxed Consistency

## Slide 20: 1 内存一致性
TSO
  Safety net: Mechanisms provided for programmers for overriding relaxations.
    For TSO, program order appears to be maintained if either the write or the read is already part of a read-modify-write(RMW) or is replaced by a read-modify-write.
    Memory barrier, also known as a membar, memory fence or fence instruction, is a type of barrier instruction that causes a CPU or compiler to enforce an ordering constraint on memory operations issued before and after the barrier instruction. (From wiki)
      eg. MFENCE guarantees that every load and store instruction that precedes the MFENCE instruction in program order becomes globally visible before any load or store instruction that follows the MFENCE instruction.
1.3 Relaxed Consistency

## Slide 21: 1 内存持久性
The Definition of Memory Persistency
  Memory persistency is an extension of consistency models for persistent memory operations.
  Memory persistency prescribes the order of persist operations with respect to one another and loads and stores, and allows the programmer to reason about guarantees on the ordering of persists with respect to system failures;
2.1 Terminology

## Slide 22: 1 内存持久性
If you mind..
  Store: The cache coherence actions required to make a write (including an NVRAM write) visible to other processors;
  Persist: The action of writing durably to NVRAM.
  Persist Atomicity: persists to each address are serialized, implying that recovery determines a unique value for each address;
  Recovery Observer: A virtual processor that atomically reads all of persistent memory at the moment of failure;
2.1 Terminology
P1
Pn
RO
……
Propagation of Store
Propagation of Persist

## Slide 23: 1 内存持久性
The Definition of Strict Persistency
  Under strict persistency, persist order observes all happens-before relations(denoted: →) implied by volatile memory order;
2.1 Strict Persistency

## Slide 24: 1 内存持久性
The Definition of Strict Persistency
  Under strict persistency, persist order observes all happens-before relations(denoted: →) implied by volatile memory order;
    Optimization: Buffered strict persistency
      Buffered strict persistency allows instruction execution to proceed ahead of persistent state, thus allowing overlap of volatile execution and serial draining of queued persist operations;
2.1 Strict Persistency
P1
Pn
RO
……
Propagation of Store
Propagation of Persist
Persistent Queue

## Slide 25: 1 内存持久性
The Definition of Epoch Persistency
  Under epoch persistency, each thread’s execution is additionally separated into persist epochs by persist barrier instructions, persists within each epoch are concurrent and may reorder or occur in parallel;
2.2 Epoch Persistency
lock (volatile mutex)
persist Qe.data[0] = x
persist Qe.data[1] = y
persist Qe.valid = true
unlock
lock (volatile mutex)
persist Qe.data[0] = x
persist Qe.data[1] = y
persist barrier
persist Qe.valid = true
unlock
D[0]
V
D[1]
D[0]
V
D[1]
Epoch 1
Epoch 2
epoch persistency
strict persistency

## Slide 26: 1 内存持久性
The History of Epoch Persistency
  Epoch persistency is similar to BPFS, but additionally allows persists to addresses protected by a lock to reorder with respect to the lock operations.
  Pros: May avoid delaying the lock release while the persist completes;
2.2 Epoch Persistency
Persist A
Persist B
VM Code
Lock
Persist Barrier
Persist B
VM Code
Persist Barrier
Persist A
New Epoch
BPFS’s Epoch

## Slide 27: 1 内存持久性
The History of Epoch Persistency
  Epoch persistency is similar to BPFS, but additionally allows persists to addresses protected by a lock to reorder with respect to the lock operations.
  Cons: Reasoning about persist order across threads can be challenging.
2.2 Epoch Persistency
Persist A
Persist B
VM Code
Lock
Unlock
Persist B
VM Code
Persist A
REAL
IDEAL

## Slide 28: 1 内存持久性
The History of Epoch Persistency
  Epoch persistency is similar to BPFS, but additionally allows persists to addresses protected by a lock to reorder with respect to the lock operations.
  Cons: Reasoning about persist order across threads can be challenging.
  Solution: Preceding and following all persists with a persist barrier.
2.2 Epoch Persistency

## Slide 29: 1 内存持久性
A Drawback of Epoch Persistency
  May incur extra constraints
2.2 Epoch Persistency
IDEAL
A
B
C
DAG-1
DAG-2
persist A
persist barrier
persist B
persist C
persist A
persist barrier
persist C
persist B
persist A
persist B
persist C
persist A
persist barrier
persist B
persist C
persist A
persist barrier
persist C
persist B
A
B
C
A
B
C

## Slide 30: 1 内存持久性
The Definition of Strand Persistency
  A strand is an interval of memory execution from a single thread separated by strand barrier instructions.
  Accesses from different strands, even from the same thread, are concurrent unless ordered by strong persist atomicity;
2.3 Strand Persistency
persist A
persist barrier
persist B
newStrand
persist C
A
B
C
Strand Persistency that Express Minimal Constraints

## Slide 31: References
[1]: S. Adve and K. Gharachorloo. Shared memory consistency models: a tutorial. Computer, 29(12):66–76, 1996.
[2]: Intel Corporation. Intel 64 Architecture Memory Ordering White Paper, Aug 2007.
[3]: Guide P. Intel® 64 and IA-32 Architectures Software Developer’s Manual[B]. Volume 3B: System programming Guide, 2011.
[4]: Pelley S, Chen P M, Wenisch T F. Memory persistency[C]// Proceeding of the International Symposium on Computer Architecture (ISCA’14). ACM, 2014:265-276.